+HELios simple test case

! The above line is necessary to tell AURORA what mode to run !

!/////////////////////////// CASE /////////////////////////!
! begin the definition of the problem by providing !
! * a x-section file name !
! * an Hermes file name to store your info !
! * a comment if you choose !
pinCell = CASE('hy047n18g110a.dat'/'H-pin.hrf'/'lab1_out')
! this example uses the 47-group neutron x-section library !

!/////////////////////// PARAMETERS //////////////////////!

$enrich = PAR("0.03") ! enrichment x/100 !
$pdratio = PAR("5") ! pitch/diameter ratio [cm] 1 =< p/d !
$duo2 = PAR("1") ! uo2 fuel diameter [cm] !
$tzr = PAR(".7/10") ! zr clad thickness [cm] !
$diameter = PAR("$duo2+2*$tzr") ! diameter of fuel + clad [cm] = fuel pin !
$rpin = PAR("$diameter/2") ! fuel pin radius [cm] !
$pitch = PAR("$diameter*$pdratio") ! pitch [cm] !
$hp = PAR("$pitch/2") ! half the pitch [cm] !
$uo2num = PAR(".0223") ! uo2 number density [1/b*cm] !
$nr = PAR("10") ! radial resolution, number of rings in fuel !
$rint = PAR("$duo2/2/$nr") ! thickness of each radial ring!
! radius of each spatial ring in fuel !
$rf1 = PAR("$rint")
$rf2 = PAR("2*$rint")
$rf3 = PAR("3*$rint")
$rf4 = PAR("4*$rint")
$rf5 = PAR("5*$rint")
$rf6 = PAR("6*$rint")
$rf7 = PAR("7*$rint")
$rf8 = PAR("8*$rint")
$rf9 = PAR("9*$rint")
$rf10 = PAR("10*$rint")

!/////////////////////// MATERIALS //////////////////////!
! define materials with a density (g/cc) !
! and a composition (weight percent) !
h2o = MAT( 1.00/ 1001, 11.1 ; 8016, 88.9 )
uo2 = MAT( /92235, "$enrich*$uo2num" ! u235 ! ;
        92238, "(1-$enrich)*$uo2num" ! u238 ! ;
        8001, "2*$uo2num" ! o16 !)
zr = MAT( / 40002, 4.29E-2 )
! You can leave the density blank and give specific atom !
! densities for each isotope. !
! There are some "special" isotopes that represent !
! blended materials: 40002 = zircaloy !

!/////////////////////// GEOMETRY /////////////////////!

! Define a pin with the radii of different regions and the !
! name of each region !
pin = CCS( "$rf1", "$rf2", "$rf3", "$rf4", "$rf5", "$rf6",
        "$rf7", "$rf8", "$rf9", "$rf10", "$rpin"
        / / fuel1, fuel2, fuel3, fuel4, fuel5, fuel6,
        fuel7, fuel8, fuel9, fuel10, clad )

! Define a simple structure with four regions surrounding a pin !
! !
! 2---------6---------3 !
! | | | !
! | _/10\_ | !
! | / \ | !
! 5----9 11----7 !
! | \_ _/ | !
! | \12/ | !
! | | | !
! 1---------8---------4 !
! !

! important data for a structure !
! * corner points !
! * other points !
! * number of corners !
! * name of background !
! * name and location of any pins (CCS) !
! * map of N-1 regions with their names !
cell = STR(("-$hp","-$hp")("-$hp",$hp)($hp,$hp)($hp,"-$hp")
       ("-$hp",0)(0,$hp)($hp,0)(0,"-$hp")
       ("-$rpin",0)(0,$rpin)($rpin,0)(0,"-$rpin")
       /4,cool/pin(0,0)/ 1,5,9,12,8,SW; 3,7,11,10,6,NE; 5,2,6,10,9,NW)

! Define the system !
unitCell = CNX(cell)
! in this simple example, you need this CNX simply to define what !
! the system is !

! define a boundary condition !
unitCell = BDRY( (1,1,1)4(0) )
! this example defines a reflecting boundary condition using 4 angles !

!////////////////// FILL MATERIALS IN GEOM //////////////!

! connect potential mappings of materials, temperatures and densities !
! with regions !
mov = OVLM(h2o/*-**/uo2/*-*-*/zr/*-*-clad)
dov = OVLD(1/*-**)
tov = OVLT(573/*-**/1273/*-*-*/623/*-*-clad)

! use those mappings !
mos = OVSM( mov )
dos = OVSD( dov )
tos = OVST( tov )

! combine mappings into a state !
! * material overlay set !
! * density overlay set !
! * temperature overlay set !
baseConfig = STAT(mos, dos, tos, 25)

!/////////////////// BURNUP /////////////////!
burnup = PATH( /(baseConfig) )

!////////////////// OUTPUT ////////////////!
! - Group structures - !
ng1 = GROUP(N/0) ! 1-group definition !
ng2 = GROUP(N/0.6,0) ! 2-group definition !
ngall = GROUP(N/) ! all (47) groups !

! - areas - !
allSmear = AREA( <*-**> ) ! spatial homgenization over entire geometry !
fuelSmear = AREA( <*-*-fuel1, *-*-fuel2, *-*-fuel3, *-*-fuel4,
        *-*-fuel5, *-*-fuel6, *-*-fuel7, *-*-fuel8,
        *-*-fuel9, *-*-fuel10> )
        ! " " " all fuel !
restSmear = AREA( <*-0-*, *-*-clad> )
        ! " " " all non-fuel!
modSmear = AREA( <*-0-*> ) ! " " " coolant only !

! This does no homogenziation, but represents a list of regions in !
! CCS 1 !
pinRadial = AREA( *-1-* )

! - stored data - !
dat2gAll = MACRO(ng2, allSmear/ dn, tr, fi, kf, ab)
dat2gFuel = MACRO(ng2,fuelSmear/ dn, tr, fi, kf, ab)
dat2gRest = MACRO(ng2,restSmear/ dn, tr, fi, kf, ab)

dat1gAll = MACRO(ng1, allSmear/ dn, tr, fi, kf, ab)
dat1gFuel = MACRO(ng1, fuelSmear/ dn, tr, fi, kf, ab)
dat1gRest = MACRO(ng1, restSmear/ dn, tr, fi, kf, ab)

datNgAll = MACRO(ngall, allSmear/ dn, tr, fi, kf, ab, p0, p1)
datNgFuel = MACRO(ngall, fuelSmear/ dn, tr, fi, kf, ab, p0, p1)
datNgMod = MACRO(ngall,restSmear/ dn, tr, fi, kf, ab, p0, p1)

! this stores one set of 2-group results for each radial region in the fuel !
fxRadial = MACRO(ng2,pinRadial/ ab)

!/////////////////// RUN /////////////////!
! the name of this object should be the same as the CASE() at the top !
pinCell = RUN(OUT : 1)