BEGIN ('Process data for output')

%OPTIONS(LINPAG=10000)
!////////////////// IMPORT CASE /////////////////!
! Load the HELIOS case named 'pinCell' from the file named 'pinCell.hrf'!
pinCell = IMP(HELIOS;pinCell/'H-pin.hrf')

! The most common comands in Zenith are: !
! SEL: select a variable from the HELIOS output and assign it to a !
! variable for use in this file !
! FOR: perform arithmetic operations on combinations of variables !
! defined with SEL command, or defined as the result of another !
! FOR command. !
! LIS: List a variable defined with the SEL or as the result of a FOR !
! command. !
! INDEX: Define an index to extract a single value from an array of !
! values. (e.g. extract the thermal flux from a 2-grp flux) !

! The following examples must be modified to match the variables you !
! used in the output section of your AURORA input file. !

!///////////// EXTRACT DATA ////////////////////!

! - BASICS k-inf vs burnup - !
! Select integral data from the status block !
Kinf = SEL(kinf /status/ pinCell;)
Kinfb = SEL(kinfb /status/ pinCell;)
Burnup = SEL(uburn /status/ pinCell;)

! *** select specific 1- and 2- and 47-group data !
! from particular MACRO blocks *** !
! - volumes - !
vA = SEL(vo / MACRO/ pinCell;dat1gAll)
vF = SEL(vo / MACRO/ pinCell;dat1gFuel)
vR = SEL(vo / MACRO/ pinCell;dat1gRest)

! - 1 Group !
nf1gA = SEL(nf / MACRO/ pinCell;dat1gAll)
nf1gF = SEL(nf / MACRO/ pinCell;dat1gFuel)
nf1gR = SEL(nf / MACRO/ pinCell;dat1gRest)
ab1gA = SEL(ab / MACRO/ pinCell;dat1gAll)
ab1gF = SEL(ab / MACRO/ pinCell;dat1gFuel)
ab1gR = SEL(ab / MACRO/ pinCell;dat1gRest)
fx1gA = SEL(fx / MACRO/ pinCell;dat1gAll)
fx1gF = SEL(fx / MACRO/ pinCell;dat1gFuel)
fx1gR = SEL(fx / MACRO/ pinCell;dat1gRest)

! - 2 Group !
nf2gA = SEL(nf / MACRO/ pinCell;dat2gAll)
nf2gF = SEL(nf / MACRO/ pinCell;dat2gFuel)
nf2gR = SEL(nf / MACRO/ pinCell;dat2gRest)
ab2gA = SEL(ab / MACRO/ pinCell;dat2gAll)
ab2gF = SEL(ab / MACRO/ pinCell;dat2gFuel)
ab2gR = SEL(ab / MACRO/ pinCell;dat2gRest)
fx2gA = SEL(fx / MACRO/ pinCell;dat2gAll)
fx2gF = SEL(fx / MACRO/ pinCell;dat2gFuel)
fx2gR = SEL(fx / MACRO/ pinCell;dat2gRest)
fx2gRad = SEL(fx / MACRO / pinCell;fxRadial)

! *** Extract specific data from the SELected data *** !
! - All indices to exract fast and thermal data - !
l2gA1 = INDEX(nf2gA/RANGE:;;;1;)
l2gA2 = INDEX(nf2gA/RANGE:;;;2;)
l2gF1 = INDEX(nf2gF/RANGE:;;;1;)
l2gF2 = INDEX(nf2gF/RANGE:;;;2;)
l2gR1 = INDEX(nf2gR/RANGE:;;;1;)
l2gR2 = INDEX(nf2gR/RANGE:;;;2;)
l2gRad1 = INDEX(fx2gRad/RANGE:;;;1;)
l2gRad2 = INDEX(fx2gRad/RANGE:;;;2;)

! - extract whole-cell-averaged data - !
nf2gA1 = FOR(nf2gA^l2gA1)
nf2gA2 = FOR(nf2gA^l2gA2)
ab2gA1 = FOR(ab2gA^l2gA1)
ab2gA2 = FOR(ab2gA^l2gA2)
fx2gA1 = FOR(fx2gA^l2gA1)
fx2gA2 = FOR(fx2gA^l2gA2)

! - extract fuel-only data - !
nf2gF1 = FOR(nf2gF^l2gF1)
nf2gF2 = FOR(nf2gF^l2gF2)
ab2gF1 = FOR(ab2gF^l2gF1)
ab2gF2 = FOR(ab2gF^l2gF2)
fx2gF1 = FOR(fx2gF^l2gF1)
fx2gF2 = FOR(fx2gF^l2gF2)

! - extract non-fuel data - !
nf2gR1 = FOR(nf2gR^l2gR1)
nf2gR2 = FOR(nf2gR^l2gR2)
ab2gR1 = FOR(ab2gR^l2gR1)
ab2gR2 = FOR(ab2gR^l2gR2)
fx2gR1 = FOR(fx2gR^l2gR1)
fx2gR2 = FOR(fx2gR^l2gR2)

! - extract radial fuel pin data - !
fx2gRad1 = FOR(fx2gRad^l2gRad1)
fx2gRad2 = FOR(fx2gRad^l2gRad2)

! *** SELect some 47-group data *** !
! - 47 group xs - !
fiNgF = SEL(fi / MACRO/ pinCell;datNgFuel)
abNgA = SEL(ab / MACRO/ pinCell;datNgAll)
abNgF = SEL(ab / MACRO/ pinCell;datNgFuel)
abNgM = SEL(ab / MACRO/ pinCell;datNgMod)
p0NgM = SEL(p0 / MACRO/ pinCell;datNgMod)
p1NgM = SEL(p1 / MACRO/ pinCell;datNgMod)
fxNgA = SEL(fx / MACRO/ pinCell;datNgAll)
fxNgF = SEL(fx / MACRO/ pinCell;datNgFuel)
fxNgM = SEL(fx / MACRO/ pinCell;datNgMod)
heg = SEL(heg/ MACRO/ pinCell;datNgMod)

! *** SELect the fluxes from each radial region in the fuel *** !
! - Radial info - !
radialFx = SEL(fx / MACRO/pinCell;fxRadial)
radialVo = SEL(vo / MACRO/pinCell;fxRadial)

!////////////// ARITHMETIC ////////////////!

! - eta - !
n = FOR(nf2gF2/ab2gF2)

! - thermal utilization - !
f1 = FOR(vF*fx2gF2*ab2gF2/(vA*fx2gA2*ab2gA2))
f2 = FOR(vF*fx2gF2*ab2gF2/(vF*fx2gF2*ab2gF2 + vR*fx2gR2*ab2gR2))

! - resonance escape probability - !
p = FOR(fx2gA2*ab2gA2/(fx1gA*ab1gA))

! - fast fission factor - !
e1 = FOR(nf1gA*fx1gA/(nf2gA2*fx2gA2))
e2 = FOR(nf1gF*fx1gF/(nf2gF2*fx2gF2))
e3 = FOR((nf2gF2*fx2gF2 + nf2gF1*fx2gF1)/(nf2gF2*fx2gF2))

! - k_inf - !
kf1e1 = FOR(n*f1*p*e1)
kf2e1 = FOR(n*f2*p*e1)
kf1e2 = FOR(n*f1*p*e2)
kf2e2 = FOR(n*f2*p*e2)
kf1e3 = FOR(n*f1*p*e3)
kf2e3 = FOR(n*f2*p*e3)
k3 = FOR(nf1gA/ab1gA)

! - multi-group - !
! 47x47 identity matrix !
ident = ARR(R: 1; 48*0; 1; 48*0; 1; 48*0; 1; 48*0; 1; 48*0; 1; 48*0; 1;
        48*0; 1; 48*0; 1; 48*0; 1; 48*0; 1; 48*0; 1; 48*0; 1;
        48*0; 1; 48*0; 1; 48*0; 1; 48*0; 1; 48*0; 1; 48*0; 1;
        48*0; 1; 48*0; 1; 48*0; 1; 48*0; 1; 48*0; 1; 48*0; 1;
        48*0; 1; 48*0; 1; 48*0; 1; 48*0; 1; 48*0; 1; 48*0; 1;
        48*0; 1; 48*0; 1; 48*0; 1; 48*0; 1; 48*0; 1; 48*0; 1;
        48*0; 1; 48*0; 1; 48*0; 1; 48*0; 1; 48*0; 1; 48*0; 1;
        48*0; 1; 48*0; 1; 48*0; 1; 48*0; 1)
p0NgStruct = IND(p0NgM/PER:RIEGO) ! store the original structure of p0 !
diag = FOR(ident^^p0NgStruct) ! create diagonal in G-O dimensions !
p0Ngtot = FOR(@SmG(p0NgM)) ! sum p0 over originating group !
p0Ngslf = FOR(@SmG(p0NgM*diag)) ! multiply by identity to extract !
        ! self-scattering !
p0Ngout = FOR(p0Ngtot - p0Ngslf) ! subtract self-scattering from tot !
p1NgStruct = IND(p1NgM/PER:RIEGO) ! store the original structure of p0 !
diag = FOR(ident^^p1NgStruct) ! create diagonal in G-O dimensions !
p1Ngtot = FOR(@SmG(p1NgM)) ! sum p0 over originating group !
p1Ngslf = FOR(@SmG(p1NgM*diag)) ! multiply by identity to extract !
        ! self-scattering !
p1Ngout = FOR(p1Ngtot - p1Ngslf) ! subtract self-scattering from tot !

pNgtot = FOR(p0Ngtot + p1Ngtot)
pNgslf = FOR(p0Ngslf + p1Ngslf)
pNgout = FOR(p0Ngout + p1Ngout)

b1 = IND(p0Ngslf/RANGE:;;1;;)
p0NgtotB1 = FOR(p0Ngtot^b1)
p0NgoutB1 = FOR(p0Ngout^b1)
p0NgslfB1 = FOR(p0Ngslf^b1)
p1NgtotB1 = FOR(p1Ngtot^b1)
p1NgoutB1 = FOR(p1Ngout^b1)
p1NgslfB1 = FOR(p1Ngslf^b1)
pNgtotB1 = FOR(pNgtot^b1)
pNgoutB1 = FOR(pNgout^b1)
pNgslfB1 = FOR(pNgslf^b1)

b1 = IND(fxNgM/RANGE:;;1;;)
fxNgMb1 = FOR(fxNgM^b1)
fxNgFb1 = FOR(fxNgF^b1)
abNgMb1 = FOR(abNgM^b1)
abNgFb1 = FOR(abNgF^b1)
perGO = IND(heg/PER:REIOG)
heo = FOR(heg^perGO)

!/////////////////// LISTS ////////////////////!
volList = LIST(vA/'Volumes'/E/E5:vA; E5:vF; E5:vR)

rpList = LIS(nf1gA/'Four factors'/E/
        E5:n;
        E5:f1;
        E5:f2;
        E5:p;
        E5:e1;
        E5:e2;
        E5:e3)

kList = LIS(nf1gA/'Different formulations of k-inf'/E/
        E5:kf1e1;
        E5:kf2e1;
        E5:kf1e2;
        E5:kf2e2;
        E5:kf1e3;
        E5:kf2e3;
        E5:Kinf;
        E5:Kinfb)

NgFxList = LIS(fxNgM/'Multi-group fluxes'/G/E5:heg;E5:fxNgM; E5:fxNgF)

NgFisList = LIS(fiNgF/'Multi-group fission'/G/E5:heg;E5:fiNgF)

NgAbList = LIS(abNgM/'Multi-group abs XS'/G/E5:heg;E5:abNgM;E5:abNgF)

NgXS01List = LIS(p0NgM/'Multi-group data (p0,p1)'/O/
        E5:heo;
        E5:p0NgtotB1 ;
        E5:p0NgoutB1 ;
        E5:p0NgslfB1 ;
        E5:p1NgtotB1 ;
        E5:p1NgoutB1 ;
        E5:p1NgslfB1 )

NgXSList = LIS(p0NgM/'Multi-group data (pTot)'/O/
        E5:heo;
        E5:pNgtotB1 ;
        E5:pNgoutB1 ;
        E5:pNgslfB1 )

FxRadList = LIS(fx2gRad/'2-Group Radial Flux Distribution'/R/
        E5:fx2gRad1; E5:fx2gRad2)

END()